Configuring the Wi-Fi Module (ESP8266 Thing)

Aim : Configure the WiFi module to connect to a local network and act as a web server to respond to requests from devices in the same network.
A request is a ping from a device to the WiFi module.
A response is the pin values of the WiFi module.

Requirements:
- SparkFun ESP8266 Thing
- SparkFun FTDI Basic
- Arduino IDE – 1.6.5 //Configured to work with SparkFun Boards

Working:

1. Setting Up -

- Start the Arduino IDE -1.6.5 as administrator. //To allow access to the serial port tab
- Power up the SparkFun thing with either a USB cable or a battery.
- Connect the FTDI basic to the serial pins of the Thing and note the port number of the basic.
- In the IDE, select the board as SparkFun ESP8266 Thing and the port number as the one noted in the above step.
- Copy the following code and paste it in the arduino sketch and hit upload.

2. Code Used -

The following code is used to configure the wifi module to act as a web server to respond to requests from devices in the same network.

// Note that the devices need to be connected to the same network as the wifi module

Edit the code according to the network in use. Set WiFiSSID[] and WiFiPSK[] variables as the ssid and password of the network.

// Include the ESP8266 WiFi library. (Works a lot like the Arduino WiFi library.)
#include <ESP8266WiFi.h>

// WiFi Definitions //
const char WiFiSSID[] = " "; //Set network specifications
const char WiFiPSK[] = " ";

// Pin Definitions //

const int LED_PIN = 5; // Thing's onboard, green LED
const int ANALOG_PIN = A0; // The only analog pin on the Thing
const int DIGITAL_PIN = 12; // Digital pin to be read

//Define pins in the similar manner if more pins are to be used.

WiFiServer server(80);

void setup()
{
  initHardware();
  connectWiFi();
  digitalWrite(LED_PIN, HIGH);
  server.begin();
}

void loop()
{
  // Check if a client has connected
  WiFiClient client = server.available();
  if (!client) {
    return;
  }

  // Read the first line of the request
  String req = client.readStringUntil('\r');
  Serial.println(req);
  client.flush();

  // Match the request
  int val = -1; // We'll use 'val' to keep track of both the
        // request type (read/set) and value if set.
  if (req.indexOf("/led/0") != -1)
    val = 0; // Will write LED low
  else if (req.indexOf("/led/1") != -1)
    val = 1; // Will write LED high
  else if (req.indexOf("/read") != -1)
    val = -2; // Will print pin reads
  // Otherwise request will be invalid. We'll say as much in HTML

  // Set GPIO5 according to the request
  if (val >= 0)
    digitalWrite(LED_PIN, val);

  client.flush();

  // Prepare the response. Start with the common header:
  String s = "HTTP/1.1 200 OK\r\n";
  s += "Content-Type: text/html\r\n\r\n";
  s += "<!DOCTYPE HTML>\r\n<html>\r\n";
  // If we're setting the LED, print out a message saying we did
  if (val >= 0)
  {
    s += "LED is now ";
    s += (val)?"on":"off";
  }
  else if (val == -2)
  { // If we're reading pins, print out those values:
Edison + wifi module + node-red/edison s += "Analog Pin = ";
    s += String(analogRead(ANALOG_PIN));
    s += "<br>"; // Go to the next line.
    s += "Digital Pin 12 = ";
    s += String(digitalRead(DIGITAL_PIN));
  } // Add pin names and pin values to the string “s” in the similar way if more pins have been defined.
  else
  {
    s += "Invalid Request.<br> Try /led/1, /led/0, or /read.";
  }
  s += "</html>\n";

  // Send the response to the client
  client.print(s);
  delay(1);
  Serial.println("Client disonnected");

  // The client will actually be disconnected
  // when the function returns and 'client' object is detroyed
}

void connectWiFi()
{
  byte ledStatus = LOW;

  // Set WiFi mode to station (as opposed to AP or AP_STA)
  WiFi.mode(WIFI_STA);

  // WiFI.begin([ssid], [passkey]) initiates a WiFI connection
  // to the stated [ssid], using the [passkey] as a WPA, WPA2,
  // or WEP passphrase.
  WiFi.begin(WiFiSSID, WiFiPSK);

  // Use the WiFi.status() function to check if the ESP8266
  // is connected to a WiFi network.
  while (WiFi.status() != WL_CONNECTED)
  {
    // Blink the LED
    digitalWrite(LED_PIN, ledStatus); // Write LED high/low
    ledStatus = (ledStatus == HIGH) ? LOW : HIGH;

    // Delays allow the ESP8266 to perform critical tasks
    // defined outside of the sketch. These tasks include
    // setting up, and maintaining, a WiFi connection.
    delay(100);
    // Potentially infinite loops are generally dangerous.
    // Add delays -- allowing the processor to perform other
    // tasks -- wherever possible.
  }
}

void initHardware()
{
  Serial.begin(115200);
  pinMode(DIGITAL_PIN, INPUT_PULLUP);
  pinMode(LED_PIN, OUTPUT);
  digitalWrite(LED_PIN, LOW);
  // Don't need to set ANALOG_PIN as input,
  // that's all it can be..
}

3. Validation -

- The LED on the wifi module shoud blink for a few seconds and should then stop blinking and glow constantly. This shows that the module is now connected to the network.
- Connect your device (which will request for the pin values from the module) to the same network as the module.
- Now, run ipscanner to identify the IP of the wifi module on the network.
  // On windows use Adavanced IP scanner
  // On linux : sudo arp-scan --interface=eth0 –localnet , wher eth0 is your device.
- Open up a browser in the device and go to the following url : IP/read (IP is the ip address of the wifi module)
- The pin values of the module would be displayed.
- Parse the pin values for further use.