ESP8266 WiFi Module and Node-RED

Aim: Configuring Node-RED via the HTTP request node to make requests to the wifi module in order to obtain the pin values from the wifi module and display it on the debug tab.

Requirements:

- SparkFun ESP8266 Thing //configured to act as a web server
- Node-RED

Working:

- Connect the pre-configured wifi module to the nework in use. The green LED should stay on.
- Connect the device (hosting node-red) to the same network.
- Start note red on the host device.
- Go to your node-red startup page (localhost:1880) and create the following flow.

Flow:

Configure the http request node as follows:
        Method : GET
        URL: http://IP/read
        //IP is the ip address of the wifi module (view confiruing wifi module documentation)
        Return: a UTF-8 string

The above request would return a string with the pin values in it. We would then have to parse the string to obtain the values. The parsing is done in the function node. The below example is to parse the analog pin and digital pin 12 of the wifi module. Other pins can be parsed similarly.

        Sample response from wifi module:

        Analog Pin = 1023
        Digital Pin = 1

The above response can be parsed by using the following function node:

var Analog = msg.payload.split("Analog Pin =")[1].split("<")[0];
var Digital = msg.payload.split("Digital Pin 12 =")[1].split("<")[0];
msg.payload = "Analog Value:" + Analog+ '\n\n\n' +"Digital Value:" + Digital;
return msg

The msg.payload now contains the analog and the digital values, which can be printed by a simple debug node.