Integration of Node-RED, Edison and ESP8266

Aim: To make request to the wifi module through the http request node in node-red running on the intel edison.

Requirements : Intel Edison //pre-configured
        ESP8266 //pre-configured

Working:

- Start intel edison on your computer.
- Connnect the edison to your network. // see edison network documentation
- Connect the wifi module to the same network. // see configuring ESP8266 doc
- Run node red on the edison // see node red on edison doc

Now, for making http requests to the wifi module, we need to know the ip addresses of the wifi module and the intel edison. For this run the following command and note down the IP addresses.
// On windows use Adavanced IP scanner
// On linux : sudo arp-scan --interface=wlan0 –localnet , wher wlan0 is your wifi network.

- Now, open the browser and enter http://IP:1880 , where IP is the ip address of intel edison.
- Make a basic flow with an http request node. //see http request node documentation

Configure the http request node as follows:

        Method : GET
        URL: http://IP/read
        //IP is the ip address of the wifi module (view confiruing wifi module documentation)
        Return: a UTF-8 string

The above request would return a string with the pin values in it. We would then have to parse the string to obtain the values. The parsing is done in the function node. The below example is to parse the analog pin and digital pin 12 of the wifi module. Other pins can be parsed similarly.

        Sample response from wifi module:

        Analog Pin = 1023;
        Digiral Pin 12 = 1;
        The above response can be parsed by using the following function node:

var Analog = msg.payload.split("Analog Pin =")[1].split("<")[0];
var Digital = msg.payload.split("Digital Pin 12 =")[1].split("<")[0];
msg.payload = "Analog Value:" + Analog+ '\n\n\n' +"Digital Value:" + Digital;
return msg

The msg.payload now contains the analog and the digital values, which can be printed by a simple debug node.